## Slide 1: PCIE SSD tool flow
Peter Xiu

## Slide 2: system overview
PLX PCIE Switch Driver
Hot Plug Extend
Backdoor Extend
General PCIE RC
AHCI inbox Driver
NVMe open source Driver
ATA PassThough
NVMe
PassThough
Uniform MPTool API
HP/PWR Control API
BD Control API
MPTool/FAE Tool/Power Cycle Tool

## Slide 3: system overview
ROM
MMIO BAR space Backdoor feature support
Firmware
Vendor Define CMD
AHCI support
NVMe support
MP Feature
Debugging Feature
HW

## Slide 4: Tool requirement
MP
  Windows 7 32bit
  PLX PCIE switch
Power Cycling
  Windows 7 32bit
  PLX PCIE switch
FAE/Debugging Tool
  Windows 7/8/8.1 32bit/64bit OS

## Slide 5: MP Flow define
Call PWR/HotPlug API to power on device
HW set Device in AHCI or NVMe mode by stripping
PCI bus driver allocate resource for each BAR of device
AHCI Driver load with no device case
NVMe Driver load with no device case
Call back door API to init DDR and download firmware from MMIO BAR space in AHCI or NVMe
ROM response backdoor feature request
Jumper to DDR , normal feature AHCI/NVMe firmware MP mode ramdisk running

## Slide 6: MP Flow define
Call HotPlug API to remove device
Call HotPlug API to insert device
PCI bus driver allocate resource for each BAR of device
AHCI Driver load
NVMe Driver load
normal feature AHCI/NVMe firmware MP mode ramdisk running:
Full feature device enumeration
Call MPTool API send command to device by pass through IF
normal feature AHCI/NVMe firmware MP mode ramdisk running:
Full feature MP and Debugging API
Call HotPlug API to remove device
Call PWR API to shutdown device

## Slide 7: MP Flow define
Call PWR/HotPlug API to power on device
PCIE SSD ready
Call PWR/HotPlug API to remove and power down device
Call PWR/HotPlug API to power on next new device